## Slide 1: Efficient Multi-image Correspondences for On-line Light Field Video Processing
Ł. Dąbała1,2, M. Ziegler3, P. Didyk1,4, F. Zilly3, J. Keinert3
K. Myszkowski1, H.-P. Seidel1, P. Rokita2, T.Ritschel5
1MPI Informatik, 2Warsaw University of Technology, 3Fraunhofer IIS,
4Saarland University, 5University College London

## Slide 2: What is a Light Field?
All Light Rays passing through a surface such as a window
Light-rays can be parameterized by 4D function:
  Position of pinhole (2 params) within 2D surface
  Position of the pixel (2 params) on 2D sensor
Virtual Camera at new position
Virtual Depth-of-Field using Synthetic Aperture

## Slide 3: Concept of Light Fields
Virtual Camera
Traditional Camera
Light Field Camera

## Slide 4: Concept of Light Fields
Light field acquisition workflows and devices based on
  Plenoptic cameras, based on micro-lens arrays (e.g. Raytrix, Lytro Illum)
  Camera arrays (IIS, Stanford)  our choice
  Cluster eye cameras, multi-aperture optics (Fraunhofer IOF, Pelican Imaging)
New possibilities for the Media Production:
  Synthetic Aperture, Refocus
  Depth Based Compositing
  Virtual Camera Movements
  Allows for 6 Degrees of Freedom VR Rendering
   Requires sufficient parallax

## Slide 5: Light Field Acquisition Using Camera Arrays
View point flexibility
  Angular
  Positional
Image quality
  Dense light field sampling
Storage and hardware resources
Sparse Array:
+ Viewpoint Flexibility
+ Storage & Resources
- Image Quality
Large Array:
+ Viewpoint Flexibility
+ Image Quality
- Storage & Resources
Small Array:
+ Image Quality
+ Storage & Resources
- Viewpoint Flexibility

## Slide 6: Our capture
9 industrial cameras (Basler acA2000-50gc)
  3x3 arrangement
Up to 16 video cameras (GoPro Hero3+ Black Edition)
  3x5 or 4x4 arrangement

## Slide 7
Upsampling a Sparse Light Field
Camera array captures sparse light field
  Not suitable for image based rendering
  Efficient way for upsampling lightfield data is required
More Images
Less Images
Less Geometry
More Geometry
Rendering with no geometry
Rendering with Explicit geometry
Rendering with Implicit geometry
Picture inspired by Chan, Shum, Ng, Image-Based Rendering and Synthesis, IEEE SIGNAL PROC. MAG., Nov. 2007
Self Calibration
Disparity Estimation
Depth Image Based Rendering

## Slide 8: Light Field depth estimation
Wanner et al. Variational Light Field Analysis for Disparity Estimation and Super-Resolution

## Slide 9: Light Field depth estimation
Wang et al. Depth Estimation with Occlusion Modeling Using Light-field Cameras
Tao et al. Depth from Combining Defocus and Correspondence Using Light-Field Cameras

## Slide 10: Large Baseline Correspondences
Yang et al. Real-Time Consensus-Based Scene Reconstruction using Commodity Graphics Hardware
Hirschmueller et al. Stereo Processing by Semi-Global Matching and Mutual Information
Rhemann et al. Fast Cost-Volume Filtering for Visual Correspondence and Beyond

## Slide 11: Pipeline Overview
Capture
Matching
Matching result

## Slide 12: Pipeline Overview
Consolidation
Consolidation result
Upsampling

## Slide 13: Preprocessing
127 | 127 | 129
126 | X | 129
127 | 131 | 131
1 | 1 | 0 | 1 | 1 | 0 | 1 | 0 | 0
X = 128
Gaussian kernel
Census transform

## Slide 14: Matching
?

## Slide 15: Matching

## Slide 16: Matching Confidence

## Slide 17: Consolidation
Problem: consistency!

## Slide 18: Consolidation
Reproject

## Slide 19: Upsampling

## Slide 20: Upsampling
What disparities should be taken to the next level?
Confidence
Proximity
Appearance

## Slide 21: Dense Light Field Results
SGM
CVF
Wang
Our method

## Slide 22: Dense Light Field Results

## Slide 23: Sparse Light Field Results

## Slide 24: Sparse Light Field Results
SGM
CVF
Our method

## Slide 25: Result videos

## Slide 26: Light Field Media Production

## Slide 27: Conclusion
Multiple depth maps for sparse light fields
Light field video processing in non offline process
Possible applications
First dataset for sparse light field video

## Slide 28: Thank You
Efficient Multi-image Correspondences for On-line Light Field Video Processing
Project page: http://resources.mpi-inf.mpg.de/LightFieldVideo/index.html
http://www.iis.fraunhofer.de/lightfield
Contact: lukasz.dabala(at)gmail.com
frederik.zilly(at)iis.fraunhofer.de